## Slide 1: Scalable Multirotor UAV Trajectory Planning using Mixed-Integer Linear Programming
Master’s Thesis defense
Jorik De Waen

## Slide 2: Problem Statement (1)
UAV Trajectory Planning
Online/Realtime <-> Offline
Fixed Wing <-> Multirotor <-> General Vehicle
Trajectory speed <-> Performance
Known <-> Unknown Environment
Flexibility?
Short Term <-> Long Term
2D <-> 3D
Notes: UAV Trajectory planning -> Many options
Online, short term planning well explored
Accurate, offline, long term planning poorly explored for multirotor UAVs
Optimality not required, wish to make it as flexible as possible
Known environments to limit scope

## Slide 3: Problem Statement (2)
Decision: use Mixed-Integer Linear Programming (MILP)
Advantages
UAV properties and movement can be modelled accurately
Solver finds optimal solution to problem
Constraint programming: flexible by design
Main Disadvantage
Performance!!!

## Slide 4: Alternative approaches
Trajectory Speed <-> Performance: main differentiator
Modified Pathplanning algorithms
  extended with kinematic constraints, post-smoothing, etc
  No (or limited) use of UAV constraints  conservative and slow trajectory
  No flexibility
Randomized approaches
  Rapidly-Exploring Random Trees, Probabilistic Roadmaps
  Take UAV dynamics into account
  Random factor adds artifacts
  TODO!!

## Slide 5: MILP Trajectory Planning

## Slide 6: Time and UAV State
Based on work by Bellingham TODO: cite everywhere!
Discretized time: N distinct time steps
UAV position, velocity, acceleration determined at each time step
John Saunders Bellingham. Coordination and control of uav fleets using mixed-integer linear programming.
PhD thesis, Massachusetts Institute of Technology, 2002.

## Slide 7: Objective Function
Objective function: minimize amount of time steps before goal is reached
UAV must reach the goal eventually
State Transition Axiom: Leslie Lamport. A simple approach to specifying concurrent systems.
Communications of the ACM, 32(1):32–45, 1989.

## Slide 8: UAV State limits
Maximum velocity: limits 2-norm of velocity vector
 Use linear approximation of 2-norm
John Saunders Bellingham. Coordination and control of uav fleets using mixed-integer linear programming.
PhD thesis, Massachusetts Institute of Technology, 2002.

## Slide 9: Obstacle Avoidance
Assume obstacles are stationary polygons, known in advance
Using Big M method:
Tom Schouwenaars, Bart De Moor, Eric Feron, and Jonathan How. Mixed integer programming for multi-vehicle path planning.
In Control Conference (ECC), 2001 European, pages 2603–2608. IEEE, 2001.

## Slide 18: Scalability issues

## Slide 19: Scenarios

## Slide 20: Pure MILP Performance Results

## Slide 21: Segmentation of the MILP problem

## Slide 22: Algorithm Approach
MILP: NP-Complete problem, for n boolean variables
Obstacles need Boolean variable for every edge for every time step
Many obstacles and/or many time steps cause bad performance
Goal of algorithm: reduce amount of obstacles and time steps
  Divide trajectory planning problem into MILP subproblems: “segmentation”
  Build trajectory gradually by solving subproblems in sequence
  Tradeoff: Optimal trajectory will probably not be found

## Slide 23: Algorithm Outline
Find Theta* path
Find turn events on Theta* path
Generate segments around turn events
Generate safe region for each segment and solve MILP subproblem sequentially
Combine sub-trajectories into final trajectory

## Slide 24: Algorithm Outline
Notes: TODO: rewrite

## Slide 25: Importance of Convexity
Integer variables determine worst case complexity
However: Solvers are smart, some problems can be solved much faster
Integer variables are needed to model non-convex search space
Working hypothesis: non-convexity of search space is “real” cause of poor performance
 Focus on keeping search space as convex as possible, instead of minimizing integer variables

## Slide 26: 1) Theta*
Extension of A* to allow path at any angle
Finds an initial path from start to goal position
  Multirotor UAV can always reach goal by following this path exactly
  Ensures a feasible trajectory can always be found
Initial path is used to find turn events, generate segments
Kenny Daniel, Alex Nash, Sven Koenig, and Ariel Felner. Theta*: Any-angle path planning on grids.
Journal of Artificial Intelligence Research, 39:533–579, 2010.

## Slide 27: Theta* Algorithm

## Slide 28: Theta* Demonstration
A
B

## Slide 29: Theta* Demonstration
A
B

## Slide 30: Theta* Demonstration
A
B

## Slide 31: Theta* Demonstration
A
B

## Slide 32: Theta* Demonstration
A
B

## Slide 33: Theta* Demonstration
A
B

## Slide 34: Theta* Demonstration
A
B

## Slide 35: Theta* Demonstration
A
B

## Slide 36: Theta* Demonstration
A
B

## Slide 37: 2) Detecting Turn Events
Segments are generated around turns in Theta* path for two reasons:
Safety/Stability
  Allows for construction of segments such that UAV can always safely navigate turns
   By starting segment well before the turn, the UAV can slow down in time
Performance
  Turns show where non-convex parts of search space are
   Max one turn per segment minimizes performance impact

## Slide 38: Safety/Stability

## Slide 39: Performance
Theta*: Node on path “survives”
   line of sight check failed
  Obstacle on inside of turn
Line between two valid positions is not entirely in search space
  Non-convex search space by definition
  Turns are manifestations of non-convex search space
Goal: Keep search space as convex as possible in each segment
   Minimize amount of turns in each segment (at most one)

## Slide 40: Turn Events Algorithm
Sometimes: multiple nodes for single turn  group into turn events
Nodes in same turn event must:
  turn in the same direction
  be close enough to each other

## Slide 41: Turn Events Algorithm

## Slide 42: Turn Events Demonstration
Start of new Turn Event:
Turns clockwise

## Slide 43: Turn Events Demonstration
Next node:
Close enough
Turns clockwise
 Add to current event

## Slide 44: Turn Events Demonstration
Next node:
Too far away
Turns clockwise
 Do not add to current event

## Slide 45: Turn Events Demonstration
Start of new Turn Event:
Turns clockwise

## Slide 46: Turn Events Demonstration
Next node:
Close enough
Turns counter-clockwise
 Do not add to current event

## Slide 47: Turn Events Demonstration
Start of new Turn Event:
Turns counter-clockwise

## Slide 48: Turn Events Demonstration

## Slide 49: 3) Generating Segments
Segments should be as small as possible, while ensuring safety
MAD: Maximum Acceleration Distance
  If segment starts 1*MAD before the turn, the UAV can always stop
  If segment starts even earlier: more room to maneuver
    Should allow for a more efficient approach
Algorithm generates 1 segment per turn event
  When turn events are far apart: generate straight segments between them

## Slide 50: Segmentation Algorithm

## Slide 54: 4) Generating the Safe Region
Not all obstacles need to be modelled in a segment
Reducing amount of obstacles improves performance
If segment has a turn: at least on obstacles prevent straight path from start to end of segment
  Those obstacles make search space non-convex
  The “important” obstacles
All other obstacles can be represented using convex constraints only
  Concept of “Safe Region”

## Slide 55: Genetic Algorithm Implementation

## Slide 56: Initial Safe Region
Orange area: convex hull of nodes in segment
Red obstacles: overlap convex hull  make search space non-convex
These are selected to be modelled in MILP problem
If UAV stays inside orange safe regions and the selected obstacles are modelled: no collisions possible
Safe region is overly restrictive

## Slide 57: Genetic Algorithm
Use genetic algorithm to grow safe region
Each individual has one chromosome with multiple genes
Each gene represents the position of a vertex of the safe region
Genetic Algorithm uses only one genetic operator:
  Can add/remove vertices
  Can “nudge” a vertex.
Tournament Selection is used, fitness function measures area of safe region

## Slide 58: Nudge operation
The safe region…
    must stay convex
    may not self-intersect
    must contain initial safe region
    may only overlap selected obstacles

## Slide 59: Expanded Safe Region
Still only overlaps red obstacles
UAV has more room to maneuver

## Slide 60: Results

## Slide 61: Testing Scenarios
Algorithm was tested on three categories of scenarios
Synthetic
  Small, hand-made, obstacles laid out to be as challenging as possible
San Francisco
  Uses real data, city grid with grid-aligned rectangles as obstacles
Leuven
  Uses real data, dense and irregular layout of polygonal obstacles

## Slide 62: Synthetic Scenarios
Up/Down Small
Up/Down Large
Spiral

## Slide 63: San Francisco Scenarios
San Francisco Small 1
San Francisco Large
San Francisco Small 2

## Slide 64: Leuven Scenarios
Leuven Small 1
Leuven Large
Leuven Small 2

## Slide 65: General Performance

## Slide 66: General Performance

## Slide 67: UAV Agility

## Slide 68: Stability

## Slide 69: Stability Issues

## Slide 70: Time Step Size

## Slide 71: Maximum Time

## Slide 72: Approach Margin and Overlap

## Slide 73: Performance
MILP solve time scales linearly with path length
  Theta* is still exponential, but much easier to solve
  “routing” aspect separated from trajectory planning aspect
MILP solve time scales exponentially with obstacle density
  Compared to total amount of obstacles for pure MILP
  Leuven scenario: just barely possible, denser than necessary
Higher UAV agility reduces solve times
  Algorithm assumes high agility of UAV
   assumption only holds for multirotor UAV

## Slide 74: Stability
Algorithm is mostly stable
  Sometimes transition between segments fails… bug, bad assumption ??
  Should be possible to fix edge cases where it fails
When trajectory is found: very similar between runs
  Theta* is deterministic  trajectory always roughly the same path
Execution time varies by 10-15% between runs

## Slide 75: Important parameters: Time Step Size & Maximum Time
Dramatic effect on performance
Coarser time step size can be solved much faster
  Solve rough trajectory first to gather info to solve fine trajectory faster?
Quick test: Pre-solve with 0,5s time step to estimate maximum time: 3x faster total solve time
Should be explored further!
  Use rough trajectory to find important edges?
  Use rough trajectory to improve transitions between segments?
  …

## Slide 76: Important parameters: Approach Margin
Some approach margin is beneficial. Larger margin: small gains
Overlapping segments:
  Significantly better trajectory
  Large performance penalty
Original idea: larger approach margin  more efficient trajectory
  Seems to be wrong. Overlapping works much better
Should be explored further!
  Why does a small overlap cause a large performance penalty?
  How can this performance penalty be minimized?
  Is there a better way to generate segments?

## Slide 77: Safe Region Generation
Genetic Algorithm was not thoroughly tested
Works well enough to not be the limiting part of the algorithm
However: probably not the best way to solve the problem
Improvements/Alternatives should be explored…

## Slide 78: Future work
Explore leads from experiments
Extend algorithm to 3D
Try Mixed-Integer Quadratic Programming so 2-norm can be modelled directly. Performance penalty or improvement?
Make complimentary online/realtime algorithm
  Necessary to use algorithm on actual physical UAV
  Further performance improvements may allow for online long-term planning?

## Slide 79: Conclusions
Goal of thesis: Build a UAV trajectory planning algorithm that scales to large and complex environments
This goal has been reached
Some weaknesses remain (segment transition bug)
Algorithm presented is just a first iteration
  experiments show several ways the algorithm could be improved
  Principles used in algorithm may be applied in other algorithms

## Slide 80: Demo

## Slide 81: Questions?